Assignment 1
Report
Dominique Roduit

1
Part 1 (pi.c)
How the problem was solved in a parallel fashion ?
To parallelize this problem, I first defined a variable chunk = samples / num_threads which indicates how much samples will be processed by each thread. Then, I just loop num_threads times (1x for each threads). In the loop, I call a new function inside_circle, whose I give the number of samples to process. The code of this function thus remains serial each thread will execute this code that simply generates random x and y coordinates, and increase the "temporary circle area" if the point is located inside it. I use the reduction on the += operator with the variable circleArea and define that the variables num_threads and chunk are shared between all the threads.

Perfomances
In running on the cluster, we can obtain the following results :
- Using 1 threads: pi = 3.14171390267876 computed in 9.733s.
- Using 2 threads: pi = 3.14167049476332 computed in 4.892s.
- Using 4 threads: pi = 3.14166019169516 computed in 2.524s.
- Using 8 threads: pi = 3.14160498290871 computed in 1.361s.
- Using 16 threads: pi = 3.14155933963597 computed in 0.6938s.
- Using 32 threads: pi = 3.14148098298714 computed in 0.581s.
- Using 64 threads: pi = 3.14150234369837 computed in 0.5009s.
- Using 128 threads: pi = 3.14150756898789 computed in 0.4932s.
- Using 256 threads: pi = 3.14162773362638 computed in 0.5658s.
Thus, we can clearly see that the time is approximately reduced by 2 every time that we increase the number of threads by 2. However, for more than 128 threads, the performance decrease again and is less good than the one with 32 threads.

Part 2 (integral.c)
How the problem was solved in a parallel fashion ?
The way I parallelized this problem is the same as for the first part. I execute a loop that calls the function getVal for each threads, passing it the number of samples to process. The code of this function remains serial and simply generate randoms x coordinates into the given interval [a,b], then sum their corresponding y coordinates. I use the reduction again on the += operator to "merge" the final result of every threads. Finally, the result is given by the formula
proposed on https://www.scratchapixel.com/lessons/mathematics-physics-for-computer-graphics/monte-carlo-methods-in-practice/monte-carlo-integration.

Performances
- Using 1 threads: integral on [5,9] = 8666.50545938244 computed in 6.561s.
- Using 2 threads: integral on [5,9] = 8666.52603997719 computed in 3.295s.
- Using 4 threads: integral on [5,9] = 8666.52479804615 computed in 1.669s.
- Using 8 threads: integral on [5,9] = 8666.60900318957 computed in 0.9524s.
- Using 16 threads: integral on [5,9] = 8666.90610599547 computed in 0.4847s.
- Using 32 threads: integral on [5,9] = 8666.82548316858 computed in 0.3979s.
- Using 64 threads: integral on [5,9] = 8666.70086830508 computed in 0.3617s.
- Using 128 threads: integral on [5,9] = 8666.65671270138 computed in 0.3397s.
- Using 256 threads: integral on [5,9] = 8666.55796557973 computed in 0.4012s.